## Slide 1: B.Tech – Computer Science and Engineering BCSE497J Lightweight Deep Learning for PCB Defect Detection (17972UG04)
Team members:
Abhinav Kumar Sinha (23BCE0565)
Janie M. Sidhikh (23BCB0020)
Atharva Rahul Tambakhe (23BCT0182)
Faculty guide :
Dr. Parthiban K (SCOPE)

## Slide 2: Aim
To systematically review and analyse recent lightweight deep learning approaches for PCB defect detection, identifying their strengths, limitations, and research gaps.
To develop and benchmark an efficient PCB defect detection framework that balances detection accuracy with real-time, edge-deployable performance.

## Slide 3: Abstract
Printed Circuit Board (PCB) defect inspection is a critical quality-control process, but manual inspection is slow, inconsistent, and difficult to scale.
Recent deep learning models, particularly lightweight YOLO and Transformer-based architectures, have significantly improved automated PCB defect detection while enabling real-time industrial applications.
This work presents a systematic review of 20 recent (2025) studies, analyzing their architectures, datasets, performance, strengths, and limitations.
Based on the identified research gaps, we propose a two-track framework comprising a lightweight edge-deployment model and a high-accuracy hybrid model for future implementation and evaluation.
The study aims to provide design guidelines, identify open research challenges, and support the development of efficient, real-world PCB defect detection systems.

## Slide 4: Literature Review - Paper Summary (1/2)
# | Paper | Objective | Methodology | Pros / Cons | Findings
1 | Improved YOLOv11s | Lightweight real-time detection | EfficientViT + C3k2 + Wise-IoU | +Fast, compact / −Synthetic validation | 92.3% mAP, 227 FPS
2 | SCF-YOLO | Edge-efficient PCB detection | MobileNetV3 + SCF + CIoU/GIoU | +Lightweight / −Limited diversity | Good speed–accuracy trade-off
3 | GESC-YOLO | Reduce model complexity | GSConv + C2f-GE + Slim Neck | +Low parameters / −Slight accuracy loss | High accuracy with fewer FLOPs
4 | GC + Adaptive Pruning | Efficient edge deployment | GroupConv + LAMP pruning | +60% smaller / −Tiny-defect loss | Better than YOLOv8n baseline
5 | MAS-YOLO | Improve small-defect detection | MECS + AHFIN + SAL | +Robust / −Higher latency | Strong multi-scale performance
6 | YOLO-DefXpert | Accurate tiny-defect detection | Improved YOLOv11 | +99% mAP / −Dataset-specific | Excellent HRIPCB results
7 | Improved YOLOv12 | Reduce misses & false alarms | GAM + BiFPN + PPA | +Higher mAP / −Higher computation | +5.8% mAP@50
8 | MSES-YOLOv10 | Detect tiny PCB defects | MSES + SPDConv + Distillation | +Compact / −Complex training | 98.9% mAP, 68 FPS
9 | Improved YOLOv8n | Embedded deployment | HFPM + DKAM + DFFN | +Lightweight / −Background sensitivity | 85 FPS, 4.57 MB
10 | Improved YOLOv8 | Better feature extraction | PConv + MLCA | +Accurate / −Private dataset | 87.3% accuracy

## Slide 5: Literature Review - Paper Summary (2/2)
# | Paper | Objective | Methodology | Pros / Cons | Findings
11 | NeoPCB-YOLO | Improve industrial accuracy | FDConv + YOLOv8 | +95.6% mAP / −FFT overhead | Outperforms YOLOv8n
12 | RF-YOLO | Improve feature extraction | RFCAConv + FDPN | +Better localization / −Added complexity | Higher detection accuracy*
13 | ABF-YOLO | Fine-grained defect detection | Axial Attention + BiFusion | +97.7% mAP / −Higher computation | Best for small defects
14 | YOLOv8x-HICAUps | Handle complex backgrounds | HorNet + CBAM + CARAFE | +Robust / −Large model | Improved detection accuracy
15 | GAN-YOLOv11 | Detect rare PCB defects | GAN + YOLOv11 | +Better generalization / −GAN training cost | 0.95 precision
16 | Enhanced YOLOv11 | High-precision detection | EMA + CARAFE + EIoU | +99.5% mAP / −More modules | 227 FPS, real-time
17 | PCB-YOLO | Lightweight high accuracy | CA + CRSCC fusion | +Compact / −Limited improvement scope | Best among lightweight models
18 | YOLO-HDEW | Improve small-defect accuracy | EMP-Attn + DSConv + P2 | +Generalizable / −Irregular defects | 98.1% accuracy
19 | YOLOv11-CGL | Lightweight deployment | CG module + LAE | +Low parameters / −Limited validation | Suitable for edge devices
20 | ViT-Mamba Fusion | Improve generalization | ViT + Mamba Attention | +Novel fusion / −Higher computation | Robust high-precision detection

## Slide 6: Research Gap
Accuracy–speed trade-off:
  Lightweight models improve inference speed, while Transformer/attention-based models improve accuracy but increase computational cost.
Limited real-world validation:
  Most studies evaluate models on single benchmark datasets with limited testing under different lighting, PCB backgrounds, and embedded hardware.
Lack of unified benchmarking:
  Existing methods are evaluated using different datasets, metrics, and experimental settings, making fair comparison difficult.

## Slide 7: Objectives
Conduct a comprehensive systematic literature review of recent PCB defect detection methods.
Compare architectures based on accuracy, FPS, model size, and computational complexity.
Analyze commonly used datasets, evaluation metrics, and deployment strategies.
Develop a lightweight framework for real-time PCB defect detection.
Evaluate the framework against recent state-of-the-art models.
SDG Goals :
SDG 9 – Industry, Innovation and Infrastructure
SDG 12 – Responsible Consumption and Production
Technology Readiness Level (TRL) : Level 2-3
Outcome : Journal (Scopus)

## Slide 8: References (1/2)
A Lightweight PCB Defect Detection Algorithm Based on an Improved YOLOv11s (2026) Xuhui Ye, Lilu Huang, Jun Wang, Xinyu Hu, Jing Xu, and Chupeng Zhang
Lightweight PCB Defect Detection Method Based on SCF-YOLO (2025) Yazhou Li, Yuanyuan Wang, Jiange Liu, Kexiao Wu, Hauwa Suieiman Abdullahi, Pinrong Lv, and Haiyan Zhang
YOLOV8X-HICAUPS: An Attention Based Approach for Accurate PCB Defect Detection (2025) Mounika M. and Gokulprasanth M.
GESC-YOLO: Improved Lightweight Printed Circuit Board Defect Detection Based Algorithm (2025) Xiangqiang Kong, Guangmin Liu, and Yanchen Gao
Lightweight PCB Defect Detection Method Based on Group Convolution and Adaptive Pruning (2025) Yuezhong Chu, Xiaolong Liu, Xuefeng Zhang, and Heng Liu
MAS-YOLO: A Lightweight Detection Algorithm for PCB Defect Detection Based on Improved YOLOv12 (2025) Xupeng Yin, Zikai Zhao, and Liguo Weng
PCB-YOLO: Enhancing PCB Surface Defect Detection with Coordinate Attention and Multi-Scale Feature Fusion (2025) Ze Wei, Fan Yang, Kezhen Zhong, and Linkun Yao
A High-Accuracy PCB Defect Detection Algorithm Based on Improved YOLOv12 (2025) Zhi Chen and Bingxiang Liu
YOLO-DefXpert: An Advanced Defect Detection on PCB Surfaces Using Improved YOLOv11 Algorithm (2025) Prabu Selvam, R. Rajasekar, C. Gunasundari, S. Janu Priya, M. Murugappan, and Muhammad E. H. Chowdhury
ABF-YOLO: A Fine-Grained PCB Defect Detection Framework Integrating Axial Attention and Bidirectional Feature Fusion (2025) Xiaoyao He and Mingyang Xie

## Slide 9: References (2/2)
YOLO-HDEW: An Efficient PCB Defect Detection Model (2025) Chuanwang Song, Yuanteng Zhou, Yinghao Ma, Qingshuo Qi, Zhaoyu Wang, and Keyong Hu
Vision Transformer and Mamba-Attention Fusion for High-Precision PCB Defect Detection (2025) Asim Niaz, Muhammad Umraiz, Shafiullah Soomro, and Kwang Nam Choi
Research on Lightweight PCB Defect Detection Algorithm Based on YOLOv11 (2025) Jiankang Yu, JiaCui Tang, and Ziming Tang
NeoPCB-YOLO: Next-Generation Enhanced Optimization YOLO for PCB (2025) Anxu Wei
PCB Defect Detection Based on Improved YOLOv8n (2025) Ao Wang, Jingyu Yan, and Zhen Wang
PCB Board Defect Detection Algorithm Based on Improved YOLOv8 (2025) Meijie Zhao, Haoyuan Xu, Saltanat Biibosunova, and Shuo Zhang
Defect Detection Network in PCB Circuit Devices Based on GAN Enhanced YOLOv11 (2025) Jiayi Huang, Feiyun Zhao, and Lieyang Chen
Enhanced YOLOv11 Framework for High Precision Defect Detection in Printed Circuit Boards (2025) Zeinab F. Elsharkawy
Small Defect Detection in Printed Circuit Boards Based on the Multiscale Edge Strengthening and an Improved YOLOv10 (2025) Weixun Chen, Xuneng Ke, and Siming Meng